## What is CAD/CAM and why should a Ham care?
## Overview of process
- CAD
  - Software to draw/design your model (2D or 3D)
  - Will leave you with some sort of picture/model file:
    - 2D: Vector file – NOT bitmap
      - Yes: SVG, DWG, possibly PDF
      - No: JPG, PNG, screenshot, scanned paper drawing…
        - At least not like that: can be traced, inspiration, etc.
    - 3D: SCAD, STEP, IGES, SLD*, F3D, etc.
    - PCB: Gerber (though you'll probably have a .BRD, .kicad_pcb, etc.)
  - Purpose of model: describe “outline” of what you've designed
    - Think home rendering
    - Tells us lots about what we want to build
      - “A panel of this by this, with a hole with this dimension here, and missing a square there with that dimension…”
      - Definition of shape and how everything is positioned relative to each other
    - No idea of how to actually build the model, just the (exact) shape.
      - Nothing about how to actually get a panel of that shape, or how to create those holes or missing squares…
- CAM - Software to translate model into paths (cutting lines) - GCode
  - Often overlooked part of the process!
    - Not File/Print!
  - From home rendering to architectural building plans
    - Even detailed rendering doesn't care about (most) details!
      - Materials (studs, joists, wiring, plumbing, etc.)
      - Structure (How does the house stand up?)
      - Process (Need foundation, then framing, then surfaces, then finish)
      - Interference (Multiple items may try to occupy the same space!)
  - CAM not a generic process
    - Specific for each type of machine and process!
      - Additive:
        - 3D printer (plastic extrusion)
        - DMLS (metal sintering)
        - SLA/DLP (light/resin)
        - SLS (light/powder)
      - Subtractive
        - Flat (2D / 2.5D)
          - Router (tool-based)
          - Laser/Waterjet/Plasma/EDM (non-tool-based)
          - Rotational
            - Lathe
          - 3D (Extra DOF)
            - Mill
    - Each machine has specific details it needs beyond simple shape and dimensions
      - Specific path details
      - Machine capabilities/limitations
      - Material details
        - Speeds and limitations
        - Tooling details (size, shape, etc.)
          - Change the tool, literally change everything
  - At this point, presentation becomes much more use-case specific
    - Additive (3D Printer) much different than Subtractive (CNC Router)
      - Machine, material, techniques, limitations, etc.
  - My perspective: desktop CNC router in wood or PCB
    - 3D printing similar concepts but very different details
- Purpose: to create detailed instructions how to build your model
  - Reflecting details of your tools and material as well as your model
- Additive: Slicer
  - Effectively fill-in layer-by-layer
  - What is the footprint in this fraction of a millimeter layer? Draw it!
    - Not quite so simple: Overhangs, underhangs, support material, bonding
    - Other subtleties: direction of strength/shear,
GCode Sender - Software to take
## CAD Options
- 3D
  - Free as in freedom
    - OpenSCAD (For us wierdos)
    - FreeCAD (For power-user types)
    - Blender (For artistic/graphical types)
  - Free as in beer
    - TinkerCAD (For a simple start)
    - OnShape (Great for collaboration)
  - I've got a budget and I'm gonna use it
    - The pay-for versions of the free-as-in-beer…
    - Fusion360 (Low-end professional CAD)
    - SolidWorks/CATIA/UG (Why are you even listening right now?!?)
- 2D
  - Resources:
    - https://www.craftsmanspace.com/free-software/free-2d-cad-software.html
  - Free as in freedom
    - Inkscape (For those used to graphics design over CAD)
    - QCAD (Includes some CAM functions as well)
    - LibreCAD (For power-user CAD types)
  - Free as in beer
    - NanoCAD (Legacy version is free but still needs yearly renewal)
    - SketchUp (For those who want easy)
  - I've got a budget and I'm gonna use it
    - The pay-for versions of the free-as-in-beer…
    - Adobe Illustrator (If you've got it, use it)